## Slide 1: NERS 551 Nuclear Reactor Dynamics Lecture 2 Jan. 11, 2022 Prof. T. Downar

## Slide 4: Time Dependent Phenomena in Nuclear Reactors
Three distinct time-dependent phenomena in nuclear reactors
  Short time phenomena: typical time intervals of milliseconds to seconds. Explicitly Solve Time Dependent Neutron Diffusion Equation w/ Delayed Neturon Source:
  Medium time phenomena: hours to days corresponding
  to the mean buildup and decay times of certain fission products
  Long time phenomena: several months or years
    Fuel depletion analysis
Cm246
Cm245
Cm244
Cm243
Cm242
Am244
Am242
Pu243
Am241
Am242m
Am243
Pu241
P240
Pu239
Pu242
Np240
Pu236
Pu238
Np239
Np238
Np237
Np236
U239
U237
U236
U235
U234
U233
U232
U238
Pa233
U231
Th233
Pa231
Pa232
Th232
Th231
Th230
Pa234
α
α
α
α
(n,3n)
(n,3n)

## Slide 5: Long Term Phenomena: Coupled Field Equations for Nuclear Reactor Depletion Simulation
Neutron Transport Equation (Steady-state)
Nuclide Depletion Equation
Thermal Fluids:
Multi-Phase Mass, Energy, Momentum

## Slide 6: Long Time Phenomena
Long time phenomena include particularly the burnup and buildup of fissionable isotopes, as well as the buildup, beta decay and burnup of fission products
Fuel burnup analysis is concerned with long-term reactor behavior which is determined by
  In-reactor fuel irradiation
  Various operations performed on fuel between burn cycles
    Discharge of burned fuel
    Shuffling of partially burned fuel
    Loading of charged fuel
Fuel burnup analysis is part of fuel cycle analysis consists of three main components
  Front-end cycle: preparation of charged fuel
  Fuel burnup analysis
  Back-end cycle: reprocessing of discharged fuel and spent fuel and/or waste treatment

## Slide 7: U-Pu Burn Chains

## Slide 8: Fuel Depletion
Uranium isotope concentrations
Plutonium isotope concentrations

## Slide 9: K-Infinity vs. Burnup (PWR)
Mwd/kg is the energy/mass generated in the FUEL
A sufficient fissile loading at BOC is needed to make the core critical throughout the cycle

## Slide 10: Fuel Depletion
Long-term evolution of the slightly enriched fuel typical of that in water-cooled reactors
Buildup of higher isotopes of plutonium and uranium that result from successive neutron captures
Conversion ratio
Effect of depletion of 235U and buildup of plutonium on reactivity
  Depletion of 235U and buildup of fission products will overwhelm the buildup of 239Pu

## Slide 11: Fuel Depletion Equations
Fuel depletion equation

## Slide 12: Medium Time Phenomena
Medium time phenomena are generally associated with the buildup, burnup, and beta decay of fission products 135Xe and 149Sm in thermal reactors
These two fission products have very large thermal neutron absorption cross sections and thus require special attention in thermal reactors

## Slide 13: Xe-135 Buildup and Decay
Buildup and burnup of 135Xe
Nuclide | Half-life | Decay constant (1/s) | Thermal XS (b) | U-235 Thermal Fission yield
Te-135 | 19.0 s | 3.64810-2 |  | 
I-135 | 6.57 hr | 2.92610-5 | 80.03 | 0.0628 (cum)
Xe-135 | 9.14 hr | 2.10710-5 | 2.665106 | 0.00256
Cs-135 | 2.3E+06 yr | 9.55510-15 | 8.663 | 4.91010-06
Ba-135 | stable | 0.0 | 5.872 | 
ENDF/B-VII.1 & NuDat 2.7

## Slide 14: Equilibrium Xe-135 Concentration
System of differential equations
I-135 and Xe-135 concentrations for constant thermal flux
  The concentrations of these isotopes quickly arise to their saturation or equilibrium values

## Slide 15: Xenon Poisoning
Reactivity effect of fission product poisoning
  Reactivity worth estimate of equilibrium Xe-135 in high flux reactors:

## Slide 16: Xe-135 Concentration after Shutdown
Using equilibrium concentrations, the time-dependent concentrations can be rewritten as
Reactor shutdown
  If the reactor has been running for several days - long enough for iodine and xenon to reach equilibrium

## Slide 17: Xenon Poisoning after Shutdown
For a sufficiently large operating flux the xenon concentration actually rises following shutdown
The peak concentration occurs at 11.3 hours after shutdown
The increase in Xe concentration causes a loss in reactivity that must be overcome if the reactor is to be restarted
Reactivity of Xe-135 Buildup after Shutdown

## Slide 18: Xe-135 Buildup and Burnout Following Step Changes of Power

## Slide 19: Sm-149 Buildup and Decay
Buildup and burnup of 149Sm
Nuclide | Half-life | Decay constant (1/s) | Thermal XS (b) | U-235 Thermal Fission yield
Nd-149 | 1.728 hr | 1.11410-5 |  | 
Pm-149 | 53.08 hr | 3.62710-6 | 1400 | 0.0108 (cum)
Sm-149 | stable | 0.0 | 4.052104 | 1.71010-12
ENDF/B-VII.1 & NuDat 2.7
Equilibrium concentrations
  The equilibrium reactivity effect of Sm-149 is on the order of 0.6% k/k
Reactor shutdown
Neodymium, Promethium

## Slide 20: Samarium Poisoning after Shutdown
Reactor shutdown (cont’d)
  If the saturation values have been reached by the time of shutdown
Reactivity effect
  Samarium concentration rises following shutdown, and at long times is greater than the saturation value by an amount pf/
  To restart the reactor after an extended shutdown, sufficient additional reactivity must be available to overcome the added samarium that resulted from the promethium decay

## Slide 21: Time Dependent Phenomena in Nuclear Reactors
Three distinct time-dependent phenomena in nuclear reactors
  Short time phenomena: typical time intervals of milliseconds to seconds. Explicitly Solve Time Dependent Neutron Diffusion Equation w/ Delayed Neturon Source:
  Medium time phenomena: hours to days corresponding
  to the mean buildup and decay times of certain fission products
  Long time phenomena: several months or years
    Fuel depletion analysis
Cm246
Cm245
Cm244
Cm243
Cm242
Am244
Am242
Pu243
Am241
Am242m
Am243
Pu241
P240
Pu239
Pu242
Np240
Pu236
Pu238
Np239
Np238
Np237
Np236
U239
U237
U236
U235
U234
U233
U232
U238
Pa233
U231
Th233
Pa231
Pa232
Th232
Th231
Th230
Pa234
α
α
α
α
(n,3n)
(n,3n)